## Slide 1: FreeRTOS introduction AJ Chen
March 11th, 2015

## Slide 2: Agenda
RTOS
FreeRTOS Directory
FreeRTOS structure
  Task
  Communication(queue)
  Interrupt
  MemMang
FreeRTOS Config Setting
Q&A

## Slide 3: RTOS
Real-Time Operating System
  Multi-Task
  Event-driven/ Time-sharing
  Accuracy
  Concerning the amount of time
  Immediate interrupt handler
Hard Real Time
  RTOS can meet a deadline deterministically
Soft Real Time
  RTOS that can usually or generally meet a dadline.

## Slide 4: FreeRTOS Directory
Foucus on folder “Source”
Check “portable” to select compiler too and witch MCU you used

## Slide 5: FreeRTOS Directory
Main files for source code
  Source/tasks.c
  Source/Queue.c
  Source/List.c
  Source/portable/[compiler]/[processor]/port.c
  Source/portable/MemMang/heap_1.c
MemMang contain sample heap implementations

## Slide 6: FreeRTOS
Source Code

## Slide 7: Task
Running
  currently utilizing the processor
Ready
  able to execute
  not currently executing
Suspended
  vTaskSuspend()
  xTaskResume()
Blocked
  vTaskDelay()
  waiting for queue and semaphore events

## Slide 8: Task TCB

## Slide 9: Queue
Communicate between tasks
xQueueSendToBlock()
xQueueRecive()
Implement mutex and semaphore

## Slide 10: Queue

## Slide 11: Interrupt
Zero is the highest interrupt priority.
configMAX_SYSCALL_INTERRUPT_PRIORITY can not be set to zero.
Setting in config file and relate function in port.c

## Slide 12: MemMang
heap management (Basic fuction below)
  pvPortMalloc( size_t xWantedSize )
  pvPortFree( void *pv )
/Source/portable/MemMang/

## Slide 13: FreeRTOS
FreeRTOS Config

## Slide 14: FreeRTOS Config
Chosen API you needed
Selection HW requirment

## Slide 15: Start FreeRTOS
Download FreeRTOS source code
if you are using the GCC compiler you can use FreeRTOS/Source/portable/GCC directory
See existing port.c and portmacro.h files for a list of such functions and macros.
Check existing sample FreeRTOSConfig.h
Implement/modify FreeRTOSConfig.h
Implement function you needed

## Slide 16: Q&A
Thanks for your time